Safe Work Method Statement

Job:.	Tank Dipping		  Client:  Billy Thorpe

Location:	415 Johns Street Bayswater……..

Date: .21 / 07 /  2007					 	Project Duration:  27 / 07 /  2007	to	29 / 07 /  2007

Principle Contractor:

Prepared By:  _John

Consultation with: 	Phillip, & 	Trish

| Tools and Equipment required | Personal Protective Equipment | Skills and Competencies Required |
| --- | --- | --- |
| Spill kit wheelie bin with reflective tape flameproof torch e-flare | Gloves High Visibility Vest (Day/Night) | First aid Manual Handling |

SAFE WORK METHOD STATEMENT

Job:.............................................................................................................................  Client:  ......................................................................................

| STEP BY STEP WORK ACTIVITY | POTENTIAL HAZARD/RISK What are the potential hazards that could cause a safety incident or injury? | CONTROL MEASURES Elimination – eliminate the work practice, plant and/or equipment responsible for the hazard. Substitution – substitute the work practice, plant and/or equipment for a safer alternative. Engineering control – redesign the work practice, use of materials, plant or equipment to attain a safer alternative. Administrative Control – change the procedures to reduce exposure (job rotation, training etc) Protective Equipment for Personnel – select appropriate equipment/apparel to reduce risk/exposure. | Name of responsible person to action |
| --- | --- | --- | --- |
| 1. Cordon off work area | Struck by vehicle Slips trips and falls Extreme weather conditions | Observe vehicle movement on the forecourt Ensure there is no evidence of a spill within the work area Step carefully over any curbs or uneven surfaces Place the wheelie bin within 2m of the dipping point Place the e-flare on top of the wheelie bin and turn the e-flare on |  |
| 2. Remove the dip pint cover plate and cap | Back strain Inhalation of fumes Tank pressurization if fuel delivery is occurring simultaneously Water accumulated in dip point enters dip channel | Face oncoming traffic- observe traffic movement on the forecourt Work within the confines of the cordoned area Squat to remove the dip point cover and keep back as straight as possible Be upwind to minimize risk of vapour inhalation Do not dip when fuel delivery is in progress Scoop any water accumulated within the dip point prior to removing dip point cap |  |
| 3. Remove dip stick and wipe clean with paper towel | Overhead hazard Fuel contact with skin | Confirm no overhead hazards within striking distance of the dip point PPE- gloves |  |
| 4. Place water finding paste onto the lower end of the dip stick Approximately 50mm from the bottom | Water finding paste contact with skin | PPE- gloves |  |
| 5. Lower the dipstick into dip point | Damage to bottom of underground tank | Gently lower dip stick into dip point Use hand over hand technique |  |
| 6. Remove dipstick. Read and record quantity of fuel and water | Poor visibility Fuel contact with skin | Use flameproof torch PPE- gloves |  |
| 7. Wipe the dipstick and dip a second time Use the average between these two dip readings as the recorded product level | Overhead hazard Fuel contact with skin | Confirm no overhead hazards within striking distance of the dip point PPE- gloves |  |
| 8. Replace dip point cap and cover plate | Back strain Pinch points | Face oncoming traffic Work within the confines of the cordoned area Squat down to replace dip point cover plate and keep back as straight as possible Stay away from pinch points on dip cap, push down with flat hand |  |
| 9. Return equipment to showroom | Struck by vehicle Manual handling Waste materials | Observe traffic movement Use correct lifting technique when collecting cones Step over kerbing carefully Dispose of paper towels in external waste bin |  |